## Slide 1: Title Lorem Ipsum
Sit Dolor Amet

## Slide 2: MCB (Miniature Circuit Breaker)
MCB is a device used to protect an electrical circuit from an overload or a short circuit.
It functions as a switch that automatically interrupts the flow of electricity when it detects a fault.
Used into low voltage electrical network instead of a fuse.

## Slide 3: Components of MCB:
1. Latch
2. Solenoid
3. Switch
4. Plunger
5. Incoming Terminal
6. Arc Chutes Holder
7. Arc Chutes
8. Dynamic Contact
9. Fixed Contact
10. Din Rail Holder
11. Outgoing Terminal
12. Bi-metallic Strip Carrier
13. Bi-metallic Strip

## Slide 4
This diagram shows how to make a single-phase MCB connection. In this circuit, we use four SP MCBs ( Single Pole Miniature Circuit Breaker ). Here we need to connect our all MCBs with phase connection and then connect the neutral line to all loads.
Connection Diagram Of MCB

## Slide 5: Construction Of MCB:
An MCB embodies complete enclosure in a module insulating material this provides mechanically strong and insulated housing
The switching system consists of a fixed incoming and outgoing wires are connected.
The operating mechanism consists of both magnetic crippling and thermal tripping arrangements.
The metal or current carrying parts are made up of electrolytic copper or silver alloy depending on the rating of the circuit breaker.
All modern MCBs are designed to handle arc interruption process where arc energy extraction and its cooling are provided by metallic arc splitter plates. These plates are held in a proper position by an insulating material. Also, arc runner is provided to force the arc that is produced between the main contacts.

## Slide 6: Working Of MCB:
Under normal working conditions, MCB operates as a switch (manual one) to make the circuit ON or OFF.
Under overload or short circuit condition, it automatically operates or trips so that current interruption takes place in the load circuit.
The visual indication of this trip can be observed by automatic movement of the operating knob to OFF position.
This automatic operation MCB can be obtained in two ways as we have seen in MCB construction; those are magnetic tripping and thermal tripping.

## Slide 7: Tripping Mechanism:
Thermal Tripping:
works as a delay fuse..
protect a circuit against a small overload that continues for a long time.
When normal current pass through bimetallic strip and rise temperature of bimetallic strip and it increase length of bimetallic strip but this expansion rate is not enough for bending movement of strip and the contacts will remain closed.

## Slide 8
II. Magnetic Tripping:
In magnetic trip MCCB an electromagnet (an iron core with a wire coil around it, forming an electromagnet) is in series with the circuit load.
With normal current, the electromagnet will not have enough electromagnetic field to attraction the trip bar for movement and the contacts will remain closed.
As High current (Short Circuit) current through the coil increases the strength of the magnetic field of the electromagnet. As soon as the current in the circuit becomes large enough, the trip bar is pulled toward the magnetic element (electromagnet), the contacts are opened and the current stops.

## Slide 9: Some Key-points to remember:
Thermal Tripping
The amount of current needed to trip the MCCB depends on the size of bimetallic Strip.
The time the bi-metal needs to bend and trip the circuit varies inversely with the current.
Tripping Action: Tripping Time will depend upon Current. The larger the overload, the faster the circuit breaker will trip
Used For: Over Load Protection
Magnetic Tripping
The amount of current needed to trip the MCCB depends on the size of the gap between the trip bar and the magnetic element.
On some MCCB this gap (trip current) are fixed and some MCCB are adjustable.
Tripping Action: A magnetic circuit breaker will trip instantly when the preset current is present.
Used For: Short Circuit Protection

## Slide 10: Uses Of MCB:
MCB is the key component for the safety and efficient functioning of electric machines.
Used in most electrical appliances that are used for industrial or domestic purposes.
In domestic usage, appliances like lights, heaters, and fans require MCB to constantly check and protect the connection.
Short Circuit Protection.
Over Load Protection.
Used in lightning circuits.
Used in switching motors.
Used in control transformers.

## Slide 11: Conclusion…
In conclusion, the Miniature Circuit Breaker (MCB) stands as a vital component in electrical systems, offering reliable protection against overloads and short circuits. Understanding its operation and importance empowers us to make informed decisions in electrical design and maintenance. Let us continue to appreciate the significance of MCBs in safeguarding both lives and equipment.

## Slide 12: Thank you for your attention!!